## Slide 1
Towards safe control parameter tuning in distributed
multi-agent systems
Julia Szewczyk, Marina Tavernier
Networked Control of Multi-agent Systems
Professor: Dominik Baumann
Advisor: Abdullah Tokmak
Aalto University, 20th May 2026

## Slide 2
Mobile robots need to navigate unstructured terrain without damaging crops and human workers
Agricultural
Swarms
Safety needed to prevent local voltage or frequency fluctuations that trigger blackouts
Smart grids
Close, high-speed formation. Needs to be robust to disturbances
Vehicle platooning
Prevention of gridlocks, protection of staff even with sudden sensor degradation
Warehouse intralogistics
High, unpredictable GPS-denied environments and sudden obstacles
Search and rescue UAVs
Real-world applications for safe distributed control
Notes: These five examples all share the same core challenge: multiple agents, limited communication, and strict safety requirements. Vehicle platooning is our simulation case — a single controller miscalibration can cause collisions. The others show this problem appears everywhere from power grids to warehouses.

## Slide 3
Paper Summary
Goal: Optimize control parameters in distributed MAS while ensuring safety and sample efficiency
Safe policy optimization problem
NEAREST-NEIGHBOR COMMUNICATION
NON-OBSERVABLE SUBSPACES
DISCONTINUOUS LOCAL REWARD
Key challenge
Control parameters of each agent j : at(j) ∈
ℝ
where
subject to
: global reward function
: safety threshold
: Safe Bayesian Optimization iteration

## Slide 4
Strong convergence but objective function needs to be known
Distributed Optimization Methods
Strong safety guarantiees using GPs but relies on global observability
Safe Bayesian Optimization
Complex policies but sample inefficient and no safety guarantees
Multi-Agent Reinforcement Learning (MARL)
Improves scalability and communication, but focuses on optimization and not on safety
Distributed Bayesian Optimization
Solution to partial observability in a purely distributed setting with safety guarantees
Our assigned paper
Related literature
Notes: Each existing approach has a critical gap. MARL needs too much data and has no safety guarantees. Distributed optimization assumes convexity which rarely holds in practice. SafeOpt has strong safety guarantees but requires centralized global observations. Our assigned paper is the first to combine all three desiderata: fully distributed, sample-efficient, and safe — made possible by introducing time as a latent variable.

## Slide 5
Paper Summary
Goal: Optimize control parameters in distributed MAS while ensuring safety and sample efficiency
Safe policy optimization problem
NEAREST-NEIGHBOR COMMUNICATION
NON-OBSERVABLE SUBSPACES
DISCONTINUOUS LOCAL REWARD
Key challenge
Control parameters of each agent j : at(j) ∈
ℝ
where
subject to
: global reward function
: safety threshold
: Safe Bayesian Optimization iteration

## Slide 6
Gaussian Processes for Safe Bayesian Optimization
Why use GPs?
Unknown reward function
Expensive real-world evaluations
Need for sample-efficient learning
Need for uncertainty estimation
SafeOpt principle
Figure by Abdullah Tokmak, Towards safe control parameter tuning in distributed multi-agent systems, 64th IEEE Conference on Decision and Control (CDC 2025), December 11, 2025
Learn with GP
Define Safe Set using LCB
Build confidence intervals
Explore safe actions only

## Slide 7
SAFEOPT
Spatio-temporal kernel
Latent variable
01
03
04
02
Paper Summary - Solution
Safe Bayesian optimization (BO) algorithm with Gaussian process (GP)
Introduce time as a latent variable to convert discontinuous local rewards into a learnable time-varying reward function
Time-varying local interpretation of global static
reward function with custom spatio-temporal kernel

## Slide 8
We instantiated independent GP models one for constraint and one for the objective
Reward-over-iteration trajectories, comparing our decoupled approach against the baseline
A single Gaussian Process modeling both objectives and constraints creates ambiguity.
Main issue
Our approach
Decoupling the GPs
Platoon simulator
Connecting the GPs
Experimental validation
One GP calculates a strict 'Safe Set,' which is then fed to the other one to safely guide the exploration of the Kp domain.
Simulator vehicle_class with scaled GP outputs to determine Kp controller gains for trucks

## Slide 9
REWARD/ITERATION
TRAJECTORIES
SPEED
ERRORS
Safety is guaranteed but strong trade-off bewteen safety and Kp exploration. Important hyperparameter tuning
Trajectories are improved with better spacing, less rubber-band effect and strong dynamic stability
Attenuated peak transient velocities. Minimized braking demands. Safer velocity convergence
Convergence to constant, non-zero steady-state error. Prioritizing safe string-stability over perfect tracking
Findings

## Slide 10
Simulations
Before
After

## Slide 11
01
02
03
05
GP models evaluated sequentially
Using localized GPs and nearest-neighbour communication
The system supports up to 8 agents under 60-second budget
Avoiding Dimensional Collapse
Sequential Linear Bottleneck
Operational Break-Points
Scalability analysis

## Slide 12
Forcing strict safety pushes the algorithm into conservative Kp exploration
Safety-Exploration trade-off
Refining of the spatio-temporal kernel to model on a better time variable
Advancing Kernel structures
Solution to single-GP instabilities and guarantees of zero-collisions
Decoupled architecture
Per-round compute time scales linearly, parallelization not needed for 8 agents
Scalability and bottlenecks
Need to provide officially verifiable safety guarantees
Formalizing safety protocols
Conclusions & Future Outlook

## Slide 13
Any questions?